## Slide 1: MyanMAR ELECTRIFICATION WORKSHOP MAY 2013
POWER FOR ALL:
THE ACCESS CHALLENGE IN INDIA for All: The Access Challenge in India
Sudeshna Banerjee
Senior Economist, Sustainable Energy Department, The World Bank

## Slide 2: Agenda for this presentation
  Section 1: Policies, Vision, and Institutional Structure
  Section 2: Achievements and Current Status
  Section 3: Challenges of RGGVY

## Slide 3: Section 1: Policies, Vision, and Institutional Structure

## Slide 4: Visions and Policies to Support Rural Electrification
Note REC – Rural Electrification Corporation; MoP – Ministry of Power; MNRE – Ministry of New and Renewable Energy, RGGVY – Rajiv Gandhi Grameen Vidyutikaran Yojana , AREP – Accelerated Rural Electrification Program; REST – Rural Electrification Supply Technology , PMGY - Pradhan Mantri Gramodaya Yojana, RVE – Remote Village Electrification
Key Milestones
Provide off-grid electricity to remote hamlets under Remote Village Electrification (RVE) (2002)
Overarching framework for rural electricity delivery and supply under Electricity Act (2003)
Goal of Universal Electricity Access within five years under National Electricity Policy (NEP) (2004)
Consolidation of all grid related programs and objective of full household electrification in five years under RGGVY (2005)
Guidelines for rural electrification under Rural Electrification Policy (2006)
Notes: The NEP specified the following goals for electricity access and supply:
Access to electricity for all households within the next five years.
Fully meeting demand through available power by 2012.
Supplying power at specified reliability and quality standards, in an efficient manner, and at reasonable rates.
Providing a minimum subsistence consumption of one kWh per household per day by 2012.

## Slide 5: RGGVY is the Flagship National Program
Provides a 90 percent capital subsidy for projects (remaining 10 percent is financed from REC loans or state finances)
Grid-based components:
Rural Electricity Distribution Backbone: Construction of 33/11 kV (or 66/11 kV) substations and lines in blocks where they do not already exist.
Village Electricity Infrastructure: Electrification of un-electrified villages and habitations (with populations greater than 100 and which can be electrified by grid power) and provision of distribution transformer of appropriate capacity in every electrified village.
Below Poverty Line (BPL) Electrification: Provision of free electrification for un-electrified BPL households. Above Poverty Line (APL) households also can approach distribution companies for connection.
Off-grid component:
Decentralized Distributed Generation (DDG): The DDG component aims to install small generators and distribution networks (based on technology neutral options) in villages in which grid extension is not cost-effective and which are not covered by the MNRE’s remote village electrification program.
Notes: The progress towards achieving these goals gained momentum with the launch of the flagship RGGVY program in 2005, consolidating all ongoing rural electrification programs at the time. RGGVY aims to electrify all villages and habitations (of more than 100 people), install small generators and distribution networks where grid extension is not cost-effective, and provide free electricity connections to BPL households. MoP retained REC as the nodal agency for implementing RGGVY. The Rural Electrification Policy of 2006 set the guidelines, definitions, and institutional structure of the RGGVY program. Complementing RGGVY is the Remote Village Electrification (RVE) program implemented by MNRE. This program, with support from state renewable energy development agencies, provides financial support for electrification of those remote non-electrified census villages and non-electrified hamlets of electrified census villages where grid-extension is either not feasible or not cost-effective and is not covered under RGGVY. Such villages are provided basic facilities for electricity/lighting through various renewable energy sources.
KJY, the Minimum Needs Program, Pradhan Mantri Gramodaya Yojana, the Accelerated Rural Electrification Program, and the Accelerated Electrification of One Lakh Villages and One Crore Households.

## Slide 6: Institutional Oversight of Rural Electrification Programs
Rural Electrification Sector does not have a dedicated Legislative Institution at the National or State level
  Rural Electrification Corporation Limited (REC) is the implementing agency for RGGVY. REC is a Central Public Sector Agency under MoP, established in 1969
  MNRE manages only off-grid agenda while MoP has oversight of both grid and off-grid agenda.
At the state level:
State Government Power Departments: RE Policies
State Electricity Regulatory Commissions: Regulation
Distribution Utilities: Service delivery and new connections
National Institutional Framework for Rural Electrification
Notes: Overall, the electricity sector is governed by two ministries at the national level—the MoP, established in 1992, and the MNRE, established in 1994. The MoP is responsible for the development of the electricity sector and implementing the landmark Electricity Act of 2003. The MNRE is in charge of the development of new and alternative energy technologies and the promotion of renewable energy. REC and MoP have overall responsibility for providing financing for grid based rural electrification. The Indian Renewable Energy Development Agency (IREDA) is the Government’s financing agency for off-grid and renewable energy based rural electrification projects. The state institutions are then responsible for implementing (and often co-financing) the electrification projects that these Central Government institutions develop and finance.
At the state level, the implementation of RGGVY rests with the state utilities that have appointed nodal officers for implementing RGGVY within their existing institutional arrangements. To a certain degree, the priority states place on rural electrification and RGGVY depends on their level of electrification.

## Slide 7: Section 2: Achievements and Current Status

## Slide 8: Village electrification stands close to 92%
Chart: Number of Electrified Villages
| 1947 | 1951 | 1961 | 1971 | 1981 | 1991 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012
Electrified Villages | 1500 | 3061 | 5170 | 106931 | 273906 | 481124 | 508043 | 489699 | 492325 | 474982 | 439800 | 459486 | 482864 | 488435 | 489527 | 500910 | 537947 | 547034
2nd_axis | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000
Chart: $ Billion
| Total Sanctioned Cost | Total Awarded Cost | Total Disbursed Cost
Cumulative Spending | 5.8729 | 7.6222 | 6.4369
Spending on RGGVY 2005-2013
Annual Rural Connections Including Below Poverty Line Consumers: 3 Million
Annual Connections to Below Poverty Consumers: 2.8 Million
Average Cost per Rural Connection: $ 350
Compensation for Free Connection for Below Poverty Line Consumers: $49
http://rggvy.gov.in/rggvy/rggvyportal/plgsheet_frame3.jsp
Notes: RGGVY is a massive distribution infrastructure program
India has spent more than $7 billion since 2005, about $1 billion a year

## Slide 9: Impressive Achievements in access expansion
India experienced a 15 percentage point increase in electrification between 2000 and 2010
28 million people have received new connections annually
70% of the new connections located in rural areas
The bottom 40% received almost half of new connections
The growth rate is highest in rural and poorest population
About 65% of the 283 million increase in new electricity users was to meet the natural population growth.
Grid-electrification constituted only 12% of total generation capacity between 2000-2010
 | 2000 | 2004 | 2010
Total | 59% | 64% | 74%
Urban | 89% | 93% | 94%
Rural | 48% | 56% | 66%
Poorest 20% | 32% | 38% | 47%
Richest 20% | 90% | 92% | 96%
Electricity Access Rates in India (% of Population), 2000-2010
Source: National Sample Survey, 2000, 2004, 2010
Number of People who Gained Access from 2000-2010, by Location and by Income Quintile

## Slide 10: Achievements Differ Across States
The lowest access rate is in Bihar at 25%, followed by Uttar Pradesh at 43%
In Uttar Pradesh and Bihar access growth has not kept pace with population growth over the last decade.
Andhra Pradesh and West Bengal experienced the greatest absolute increase of more than 10 million in electrified population beyond population growth during this period.
Uttarakhand grew at the fastest pace, at 6 percent annually, followed by Jharkhand at 4.3 percent. A majority of states grew their electrified population annually by 2-4 percent.
Access Rate across States and Union Territories, 2010
Incremental Cumulative Access across States, 2000-2010
Chart: Number of states and UTs
| Rural | Urban | Poorest | Quintile 2 | Quintile 3 | Quintile 4 | Richest | Total
<25% | 5 | 0 | 6 | 4 | 2 | 1 | 0 | 2
Between 25% and 50% | 5 | 1 | 11 | 9 | 6 | 1 | 0 | 5
Between 50% and 75% | 6 | 4 | 5 | 8 | 7 | 11 | 4 | 7
More than 75% | 19 | 30 | 13 | 14 | 20 | 22 | 31 | 21
Chart: Million
| Uttar Pra and Uttarakhand | Madhya Pradesh and Chattisgarh | Bihar and Jharkhand | West Bengal | Andhra Pradesh | Maharashtra | Rajasthan | Tamil Nadu | Karnataka | Gujarat | Orissa | Kerala | Assam | Haryana | Other States
Number of people gaining access between 2000-2010 (millions) | 34.3625 | 33.3695 | 31.395 | 25.8261 | 24.2447 | 22.6671 | 20.2318 | 20.0986 | 17.7449 | 14.5137 | 13.7335 | 8.3383 | 7.5798 | 6.816 | 17.0309
Source: National Sample Survey, 2000, 2004, 2010
Notes: Total: A little above half states are above 75%
Urban: most states are above 75%
Rural: Half the states are above 75%
Bihar is the worst one with 25% access rate followed by UP at 47%
Uttar Pradesh (with Uttarakhand), Bihar (with Jharkhand), Madhya Pradesh (with Chhattisgarh), West Bengal, and Andhra Pradesh are success stories in expanding access, accounting for 52 percent of the incremental growth in electrified population.

## Slide 11: Still, More than 300 million Still Don’t Use Electricity
93% percent of unconnected live in rural areas
70% of the unconnected are in bottom 40% of income ladder
Average monthly household electricity consumption (across electrified households) is 76 kWh/month.
Rural households consume 54 kWh/month on average -about half of what the average urban household consumes
Kerosene is the main alternate fuel source for lighting
Use of kerosene is highest at 52% in the poorest quintile. In all the other quintiles, use of electricity is relatively higher compared to kerosene
Source: National Sample Survey, 2010
Notes: Unconnected live in 5 states

## Slide 12: Grim Picture of Electricity Reliability in India’s Villages
Only about 7% of rural households have no outages, and 18 % indicate that they do have power outages for up to four hours per day, but no more
Bihar and UP - States with lower electrification rate also face highest hours of outages per day
For communities that have 1 to 5 hours of service outage the adoption rate is about 72%, compared to over 80% for those with the highest reliability or no outages at all
Reliability and adoption rate for villages with electricity
Source: India Human Development Survey 2005.
Note: The category 0 = 3.4% of villages; 1-5 = 19.3% of villages, 6-10 = 26.2% of villages, 11-15 = 23.7% of villages, 16-20 = 25.0% of villages and 21-24 = 2.4% of villages.
Chart: %
| Rural unelectrified households in unelectrified villages | Rural unelectrified households in electrified villages | Rural electrified households in electrified villages
% of HHs using kerosene | 89.7 | 83.9 | 69.8
Notes: Number of people who do not have electricity is actually higher, India has been successful in expanding connections but not ensuring electrons flow through wires

## Slide 13: Section 3: Challenges of RGGVY

## Slide 14: RGGVY Norms and Exclusions impose implementation challenges
Connection kit (comprising of a Meter, Mechanical Circuit Breaker, a Switch and a CFL holder with a bulb) when fixed at outer wall (e.g. AP) forces extension of loads, when fixed inside house (e.g. ODISHA) reading meter becomes difficult
Central Public Sector Agencies engaged in RGGVY lack expertise in distribution projects and awareness of the local geographical and socio-economic context.
State utilities engaged in RGGVY have lacked the project management expertise and large manpower
RGGVY’s provision of free connections only to BPL households has also challenged the timely and cost-effective completion of RGGVY projects.
The REC cost norms were highly standardized and did not vary by geography, cost of living, or other significant local factors
Many states have installed transformers that do not have adequate capacity to accommodate the full village load
Most households charged on estimated basis and meters are often not installed
Notes:   CPSUs - Have relied on local private (“turnkey”) contractors.
  Have terminated several contracts on the basis of non-performance.
  and thus are more easily overwhelmed by the substantial number of households encompassed by RGGVY
  More broadly, RGGVY efforts have focused on simply establishing electricity infrastructure and have largely ignored the proportionate investments necessary to ensure rural supply quality and reliability.
  The REC cost norms were highly standardized and did not vary by geography (other than to distinguish between plain areas and hill/desert/tribal areas), cost of living, or other significant local factors and often were lower than the costs originally estimated in the state DPRs

## Slide 15: Rural Electrification is not Commercially Viable
The revenue billed to customers typically do not cover the full cost of providing rural supply.
  Average revenue billed to rural consumers was between 16 and 65 percent of the estimated cost of rural supply
  The loss to the utility to supply rural consumers is about Rs 3.6/kWh ($ 0.08).
  Highest loss is in Rs 7.5/kWh ($0.18) in Bihar – the state with the lowest access rate
The total burden from serving rural consumers in 2010 was just under Rs 200 ($4.4) billion
The financial burden from serving rural consumers is the highest in states such as Tamil Nadu, UP, Bihar, Andhra Pradesh
Revenues and Costs of Rural Service Delivery
Source: PricewaterhouseCoopers, 2012
Financial Burden from Serving Rural Consumers (2010)
Notes: Tariffs paid by customers that do connect to the grid typically do not cover the full cost of providing rural supply  particularly an issue with BPL households that often pay lower tariffs than other consumers (it is exacerbated by RGGVY’s focus on providing BPL connections), but is also an issue with APL households
The total burden from serving rural consumers in 2010 was just under ` 200 ($4.4) billion across these twelve states. Losses ranged from ` 3.1 ($ 0.1) billion in Uttarakhand to ` 36 ($ 0.8) billion in Tamil Nadu This loss figure is estimated by calculating the product of the total number of rural consumers (using NSS 2010 data) and the gap between average revenue and average cost.

## Slide 16: Private sector participation in rural electrification is limited
There are more than 37,000 rural franchisees in operation, covering more than 216,000 villages across 18 States in the country
An overwhelming majority are revenue collection franchisees
There are a few ‘input-based’ franchises, where the franchisee purchases the energy that is input into the franchise area, and then resells that energy to consumers
The most notable version for the rural input-based approach is the Single Point Power Supply scheme
The rural SPPS franchisee sells power to consumers at tariffs approved by the regulator, and pays a fixed fee to the distribution licensee.
Notes: This fee is worked out by the licensee considering 10 percent of Low Voltage Line Losses, a commission/profit of 15 percent for the franchisee, and a Low Voltage Line maintenance allowance of two percent. Additionally, the licensee offers the franchisee an incentive of 2 percent on timely payment of its bills and a cash incentive (of Rs. 100) per new connection issued through the franchisee.

## Slide 17: Key Lessons
What to take away from Indian experience
National vision and policy framework
Integrated capital funding mandate
Project management and quality control framework
Free connections to poorest consumers
What NOT to take away from Indian experience
Role of planning
Clear allocation of roles and responsibilities
Importance of physical and commercial sustainability
Artificial distinction of consumers based on poverty line
Huge spread of infrastructure but poor electricity supply